## 4 X Idler Assembly
### Vitamins
2 Ball bearing 624 4mm x 13mm x 5mm / 2 RJ4JP-01-08 Bushing / 1 M3 cap screw x 35mm / 1 M4 cap screw x 25mm / 1 M3 cap screw x 18mm / 1 Nyloc nut M3	1 Nyloc nut M4 / 2 Washer M3 x 7mm x 0.5mm / 2 Washer M4 x 9mm x 0.8mm / 1 Nut M3 / 1 M5 Brass nut

### Printed
1 i3xends_v2_Idler.stl	1 i3xends_v2_Idler_fork.stl	1 z_screw_isolator_left.stl

### Assembly

1. Slide the 2 Idler parts together, they are a VERY tight fit. Don’t worry if they don’t slide completely together. When inserting the X rods they will home the last bit.
2. Insert a M3 Nut in the idler fork. Slide it in the idler bits and insert a M3 35mm cap screw and nut from the end of the idler, make sure the screw engange the nut corretcly.
3. Insert the M4 screw and washer through the fork while adding in the following order: 2 624 bearings. Once the screw is through add the final M4 washer and then M4 nyloc
4. Insert 2 RJ4JP-01-08 Bushing, one from the top and one from the bottom.
5. Insert a M5 brass nut in the isolator. Put a M3 nut and washer through the isolator and a M3 Nyloc on the other side.