## Y motor assembly
### Vitamins
4 M4 cap screw x 16mm / 1 NEMA17 x 47mm stepper motor / 4 Nyloc nut M4 / 4 M3 cap screw x 10mm	1 GT2 pulley 20 teeth / 4 Washer M3 x 7mm x 0.5mm / 4 Washer M4 x 9mm x 0.8mm / 4 Star washer M3 x 0.5mm

### Printed parts
  1 y_motor_bracket.stl

### Assembly

Assemble as shown above with the motor shaft protruding 3mm from the pulley. The wires should be twisted in pairs (as described for the Z motors) and exit up or sideways.