## Y Heatshield Assembly
The heatshield insulates the bottom surface of the heated bed to allow it to get hot enough for ABS. It isn't needed for printing PLA . If you want to print ABS it can be added later as it just slides under the bed. It is simply made from enough layers of corrugated cardboard to fill the air gap. The bottom layer has holes cut in it to clear the screws heads on the y-carriage and a slot to clear the ribbon cable. The higher layers just need the slot. The top layer will need an additional slot to clear the thermistor.
### Vitamins
  1 Corrugated cardboard 192mm x 216mm x 5mm (cut it from the box of the kit).
### Assembly

Start by printing a paper template from the pdf drawing y_heatshield.pdf. Cut out the outline with scissors or a craft knife. Align the corrugations with the X axis for less heat loss as the bed moves and maximum heat loss from the bed fan if fitted. Place the template over the cardboard and cut round with a straight edge and craft knife. Cut through the holes.

The cut three more sheets the same size and cut slots to clear the ribbon cable and one in the top one to clear the thermistor.