## 20. X Axis Assembly
### Vitamins
2 Smooth rod 8mm x 381mm	2 Wing-nut M4

### Sub-assemblies
1 extruder_assembly	1 x_carriage_assembly	1 x_carriage_fan_assembly

### Assembly

1. Remove the bar clamps at the top
2. Take the X motor end and drill the holes for the smooth rod with a sharp 8mm drill
3. Slide in the smooth rods. They should go in 42mm
4. Slide on the X carriage
5. Press on the Idler end so there is 299mm smooth rod between the Motor end and the idler
6. Place this assembly on top of the Z smooth rods and lower it slowly. It takes some fiddle work to make the 2 smooth rod and threaded rods go in
7. Lower the assembly down to the Z isolators
8. Refit the bar clamps