## 5 X Motor Assembly
### Vitamins
36 Washer M3 x 7mm x 0.5mm / 1 GT2 pulley 20 teeth / 2 RJ4JP-01-08 Bushings / 1 NEMA17 x 47mm stepper motor / 2 Nut M3 / 1 M3 cap screw x 18mm / 2 M3 cap screw x 12mm	2 No2 pan wood screw x 13mm / 2 Washer M2.5 x 5.9mm x 0.5mm / 1 Microswitch / 1 M5 Brass nut / 1 Nyloc nut M3

### Printed parts
1 d_shell.stl	1 d_shell_lid.stl	1 z_screw_isolator_right.stl

### Assembly
1. Slide the 2 Idler parts together, they are a VERY tight fit. Don’t worry if they don’t slide completely together. When inserting the X rods they will home the last bit.
2. Attach the stepper with the wires facing down. Use enough washers that the base of the stepper clears the inside of the motor mount plus 1mm.
3. Slide on the pulley on and center it in the motor mount channel with a 1mm gap to the base of the stepper.
TIP: The goal is that the pulley can sit centered in the belt channel. You might need to add 1 more washer on each of the 3 screws for the motor
1. Insert 2 RJ4JP-01-08 Bushings, one from the top and one from the bottom.
2. Insert 2 M3 nuts in the endstop and insert 2 M3 screws and washers
3. Attach the microswitch with the wood screws and washers
4. Insert a M5 brass nut in the isolator. Put a M3 nut and washer through the isolator and a M3 Nyloc on the other side.
5. Bundle up motor wires.