## 7. Z Axis Assembly
### Vitamins
2 M3 cap screw x 16mm / 4 M4 cap screw x 16mm / 2 Nyloc nut M3 / 4 Nyloc nut M4	2 Smooth rod 8mm x 336mm / 2 Threaded rod M6 x 300mm / 2 Washer M3 x 7mm x 0.5mm / 4 Washer M4 x 9mm x 0.8mm

### Printed parts
2 z_bar_clamp.stl	2 z_screw_pointer.stl

### Sub-assemblies
1 x_motor_assembly	1 x_idler_assembly	2 z_motor_assemblies

### Assembly

1. Insert the M3 nyloc nuts into the nut traps inside the bar clamps and M4 nylocs into their base.
  TIP: add 1-2 washers in the gap and use a screw that is long enough to go all the way through the clamp and catch the nut.. use the screw to guide it in to the nut trap. Use the final screw with the washers in place to gently home the nut. Remove the washers in the gap
2. Fit M3 x 16mm cap screws and washers to the bar clamps.
3. Attach the bar clamps to the top of the gantry using M4 x 16mm cap screws, note that they both face the same way, i.e. they are not symmetrical. Leave the screws loose.
4. Fit the Z bars (smooth rods), inserting them through the X ends. Tighten the left hand bar clamp but leave the right hand one loose.
5. Thread the isolators onto the bottom of the lead screws (threaded rod) about 100mm of the way up.
6. Screw the Z screw pointers on the bottom just high enough to clear the couplings
7. Push each X end to the top and insert the lead screw from underneath far enough to allow the bottom end to go into the top of the couplings.
8. Orientate the couplings so that the flat on the motor shaft is facing towards the gap and then tighten the screws.