## 5 X Motor Assembly
### Vitamins
6 M3 cap screw x 16mm / 8 M3 cap screw x 20mm / 2 M3 cap screw x 20mm / 1 15 way D IDC socket / 2 M3 x 6mm grub screws (pre-fitted to pulley) / 2 M3 cap screw x 45mm / 2 LM8UU linear bearing / 1 NEMA17 x 47mm stepper motor / 14 Nyloc nut M3 / 2 Nitrile O-ring 2.5mm x 1.6mm / 1 Polypropylene strip 394mm x 18mm x 0.5mm	1 Polypropylene strip 456mm x 25mm x 0.5mm / 2 M3 pan screw x 8mm / 4 No2 pan wood screw x 13mm / 1 GT2 pulley 20 teeth / 1 Ribbon cable 20 way 1220mm / 1 Microswitch / 4 Heatshrink sleeving ID 2.4mm x 15mm / 4 Washer M2.5 x 5.9mm x 0.5mm / 22 Washer M3 x 7mm x 0.5mm / 2 Star washer M3 x 0.5mm

### Printed parts
1 d_shell.stl	1 d_shell_lid.stl	1 z_screw_isolator_right.stl

### Assembly
1. Slide the 2 Idler parts together, they are a VERY tight fit. Don’t worry if they don’t slide completely together. When inserting the X rods they will home the last bit.
2. Attach the stepper with the wires facing down. Use enough washers that the base of the stepper clears the inside of the motor mount plus 1mm.
3. Slide on the pulley on and center it in the motor mount channel with a 1mm gap to the base of the stepper.
4. Insert 2 LM8UU bearings, one from the top and one from the bottom.
5. Insert 2 M3 nuts in the endstop and insert 2 M3 screws and washers
6. Attach the microswitch with the wood screws and washers
7. Insert a M5 brass nut in the isolator. Put a M3 nut and washer through the isolator and a M3 Nyloc on the other side.