## 1. General Build Tips
- X is left / right. Y is backwards / forwards. Z is up / down.
- De-grease the rods. Acetone or methylated spirit works. Dont worrie they will be oiled later.
- All screws have a plain washer where they meet the plastic/sheets, to spread the load and prevent the plastic being chewed up by the rotation of the screw head. Most fixings have a captive Nyloc nut to prevent them vibrating loose. It is very important that the nut is fully seated in the nut trap while the screw is inserted. They are quite a tight fit, so sometimes it is necessary to pull or push them in with a long screw.
- The X and Y bar clamps should not be over tightened, i.e. do not close the gap fully or the parts will break. The Y and Z bars only need a light clamping force because the only force trying to slide them is the bearing friction.
- Washers tend to have a smooth side and a side with a burr from being stamped out. Make sure the smooth side faces bearings and belts.

NOTE: During this manual 3mm fiberboard was used. It’s cheaper for prototyping.

NOTE: It’s optional, but might be a good idea to drill all holes to their spec’ed size. If a 4mm screw is used in the hole drill it to 4mm. Endstop switches are mounted with No2 Wood screws and a 2mm predrill is recommended

### Tools Required
- Allen keys: 2.5mm & 3mm
- Needle nose pliers.
- 8mm sharp drill bit
- 3mm
- 4mm
- 2mm
- Drill with variable speed
- Small hammer
- Marker or pen
- M3 tap
- Wire cutters.
- Wire strippers.
- Crimp tool for dupont connectors – You can solder but its not nearly as good as crimping
#### Recommended
- Multi-meter
- Digital callipers.
- Dial gauge and/or Set of feeler blades(to level the bed more - precise than paper method)
- Heat gun for heat shrink tubing… far better than lighter or soldering iron
- Ruler and square. Even thou it should be 90 degrees, it does not hurt to check.
#### Consumables
oil, white lithium grease, alcohol (for cleaning bed), lint free wipes.